MATERIAL SAFETY DATA SHEET				Page 1

From:   C A R   K E M   P R O D U C T S,  I N C.

4275 St. Johns Parkway

Sanford, FL 32771

(800) 423-3168

Emergency phone #: (800) 424-9300 CHEMTREC

# To comply with OSHA form #174

SECTION 1 – IDENTIFICATION OF PRODUCT

Product Name:			CAR FRESH

Product Code:			A-33

Synonym or Cross Reference:	Hydrocarbon Mixture

SECTION II – HAZARDOUS INGREDIENTS

Ingredients:			OSHA	PEL	ACGIH		TLV		OTHER	LIMITS %

Hydotreated Light Petroleum Distillate					64742-47-8

Butane/Propane/Isobutane Propellent 1000PPM 800PPM

(106-97-8) (74-98-6) (75-28-5)

Supplier Notification: This product contains the following toxic chemicals subject to the reporting requirements of section 313 of the emergency

Planning & community right to know act of 1986 & of 40 CFR 372:

CAS		Chemical Name		% by Weight

N/A		N/A

SECTION III – PHYSICAL DATA

Appearance: 			Clear Liquid		Vapor Density;		N.E.

Odor:				Pleasant			Evaporation Rate:	(Air-1)	N.E.

Specific Gravity  (H20=1)		0.8			Solubility In Water:	None

Vapor Pressure (mmHg):		N.E.

Boiling Point:			N/A

SECTION IV – FIRE AND EXPLOSION DATA

Flash Point:			193 F TCC

Fire Extinguishing Media:		Regular foam, CO2, Dry Chemical

Special Fire Fighting Procedures:	Firefighters: wear self-contained breathing apparatus. Cool fire exposed aerosol containers with water.

Unusual Fire and Explosion Hazard:	Flame extension test. Contents under pressure! Exposure to temperatures above 120F may cause bursting.

SECTION V – HEALTH HAZARD / TOXICOLOGICAL PROPERTIES

Threshold limit value	: not established

Carcinogenicity		: NTP/IHRC/OSHA: No, No, No

Health Hazards Acute/Chronic:

Overexposure by inhalation may cause irritation, dizziness, nausea, headache and even loss of  consciousness.  Aspiration may be a hazard.

May be harmful or fatal if swallowed.

### F  I  R  S T  A I D

Inhalation:   Move person to fresh air.  If breathing stops, administer artificial respiration.  Get medical attention immediately.

Ingestion:     Do not induce vomiting. Contact a physician immediately.

Eye contact: Flush eyes immediately with large amount of water for 15 minutes, lifting eyelids occasionally. Get medical attention at once.

Skin contact: Remove contaminated clothing and immediately wash exposed area with water for 15 minutes. Get medical attention if necessary.

MATERIAL SAFETY DATA SHEET				Page 2

From:   C A R  K E M  P R O D U C T S,  I N C.

4275 St. Johns Parkway

Sanford, FL 32771

(800) 423-3168

Emergency phone #: (800) 424-9300 CHEMTREC

#### Product Name: 	A-33   CAR FRESH

SECTION VI – REACTIVITY DATA

Stability:				Stable

Conditions To Avoid:		Extreme Temperatures

Polymerization:			Will not occur

Conditions to avoid:		None

Incompatible Materials:		Strong acids and oxidizers

Hazardous Decomposition or by-products: Carbon Dioxide, Carbon Monoxide

SECTION VII – SPILL AND DISPOSAL PROCEDURE

In case material is released or spilled: ventilate area and avoid breathing vapors.  Dike & contain spill with inert absorbent material & place

in sealed container for disposal.

Waste disposal method: Replace cap & discard container in accordance with all approved procedures set forth by Federal,State, Local Authorities.

Precautions to take in handling & storage: Mop up residue & keep runoffs out of sewer. Keep at room temperature away from direct sunlight.

Other precautions: Flammable.  Contents under pressure.  Do not puncture or incinerate container.

SECTION VIII – PROTECTION INFORMATION

Respiratory Protection:	None required with adequate venting

Ventilation:		Equivalent to outdoors

Protection Gloves:		Recommended

Eye Protection:		Recommended

Other protective equip:	Keep out of reach of children.

SECTION IX – ADDITIONAL INFORMATION

Product Code: 	A-33	Prepared on:	09/2003

This information in the Material Safety Data Sheet has been compiled from our experience and date presented in various technical publications.

It is the user’s responsibility to determine the suitability of this information for the adoption of the safety precautions as may be necessary.

We reserve the right to revise Material Safety Data Sheets from time to time as new technical information becomes available.  The user has the responsibility to contact the company to make sure that the sheet is the latest issue.